## Slide 1
SESSION 2: LITERATURE MAP & METHOD OUTLINE
Mapping the Research Gap to a
Bayesian Fusion + GP Mapping Method
Human–Robot Collaborative Hygiene Monitoring and Surface Disinfection
Presented by : Team 1

## Slide 2
Review Scope
Five works spanning shared autonomy, verification, vision-based cleaning, device reprocessing, and HRC adoption
[1]
Shared Autonomy Disinfection
Sanchez & Smart, 2021
[2]
Verifiable UV Disinfection
Sanchez & Smart, 2022
[3]
Vision-Based Mobile Manipulation (DeKonBot)
Baumgarten et al., 2022
[4]
RODI: Robot-Supported Device Reprocessing
JARVIS Project, 2021
[5]
HRC in Healthcare: Narrative Review
Weerarathna et al., 2023
Each work is assessed against four lenses: contamination sensing, cleanliness verification, sensor fusion depth, and spatial mapping coverage.

## Slide 3
Literature Comparison Matrix
Capability coverage across the five reviewed systems
Work
Contamination
Sensing
Cleanliness
Verification
Multi-Sensor
Fusion
Spatial
Mapping
Uncertainty
Quantified
[1] Sanchez & Smart
(2021)
✗
✗
✗
✗
✗
[2] Sanchez & Smart
(2022)
✗
◐
✗
✗
✗
[3] Baumgarten et al.
(2022)
◐
✗
✗
✗
✗
[4] RODI / JARVIS
(2021)
✗
✗
✗
✗
✗
[5] Weerarathna et al.
(2023)
—
—
—
—
—
Proposed
Framework
✓
✓
✓
✓
✓
[5] is a narrative review (no system to score) — included to frame human-factors context, not technical capability.

## Slide 4
What Each Paper Contributes — and Misses
[1]
Contributes:
Operator-designated surfaces; autonomous UV motion execution
Misses:
No automatic detection; no hygiene map; no uncertainty model
[2]
Contributes:
Rigorous UV irradiance modeling; dose logging vs. target
Misses:
Verification is path-level, not biological; no sensor fusion
[3]
Contributes:
CNN + point-cloud localization of high-touch objects (45 tested)
Misses:
No contamination level estimate; relies on fixed motion templates
[4]
Contributes:
Structured device-reprocessing workflow automation
Misses:
Pilot description only; no mathematical contamination model

## Slide 5
Closing the Gap
Each literature gap maps directly to a component of the proposed method
No contamination estimation
Bayesian multi-sensor fusion
Weak / path-level verification
Per-patch posterior + uncertainty
Sensor fusion in isolation
Closed-form inverse-variance fusion
No spatial coverage of unobserved areas
GP regression w/ RBF kernel
HRC is perception-limited
Uncertainty-aware HRC decision rules

## Slide 6
Method Outline
From raw sensor data to a hygiene map to a robot action
1. Surface Discretization
Surface split into N patches s_i with 2D coordinates; contamination f_i ∈ [0,1] per patch.
2. Sensor Measurement
RGB-D, fluorescence, hyperspectral & UV-dose models each give a noisy reading z = f_i + ε.
3. Bayesian Fusion
Inverse-variance weighting yields a closed-form fused posterior mean μ and variance σ² per patch.
4. GP Spatial Mapping
RBF-kernel GP propagates fused posteriors to unobserved patches with calibrated uncertainty.
5. Decision Policy
Priority score, adaptive UV dose, and 4 threshold-based HRC rules drive robot action.

## Slide 7
Method Detail — Bayesian Fusion
Closed-form Gaussian update
Measurement model:
z_m,i = f_i + ε_m, ε_m ~ N(0, σ²_m)
Fused precision:
σ⁻²_fused = σ⁻²₀ + Σ σ⁻²_m
Fused mean:
μ_fused = σ²_fused · (μ₀/σ²₀ + Σ z_m/σ²_m)
Key guarantee: σ²_fused < σ²_m for every sensor m — adding sensors never increases uncertainty, even noisy ones.
Sensor noise variances used
Fluorescence
σ² = 0.01
Most precise — biologically specific
RGB-D
σ² = 0.04
Noisiest — affected by lighting/specularity
Prior belief
σ² = 0.09
Neutral starting assumption (μ₀ = 0.5)

## Slide 8
Method Detail — Gaussian Process Mapping
RBF kernel
k(xᵢ, xⱼ) = σ²_f · exp( −‖xᵢ − xⱼ‖² / 2l² )
Length-scale l = 1.0 controls how fast spatial correlation decays with distance.
GP posterior
μ* = Kᵀ* (K + Σₙ)⁻¹ y
Σ* = K** − Kᵀ* (K + Σₙ)⁻¹ K*
Every patch — observed or not — receives a mean estimate and a calibrated uncertainty. Unobserved patches inherit higher variance, exactly where human confirmation should be sought.
Distance vs. spatial correlation (l = 1.0)
Distance d
Correlation
1 unit
exp(−0.5) = 0.607
2 units
exp(−2) = 0.135
√2 units
exp(−1) = 0.368
Closer patches are treated as more correlated — contamination near a known hotspot is assumed to spread locally, decaying smoothly with distance.

## Slide 9
Validation Case: 3×3 Surface Grid
5 observed patches (Bayesian fusion) + 4 unobserved patches (GP-estimated)
Patch 7
GP estimate
~0.80
Confirm
Patch 8
Observed
0.702
Disinfect
Patch 9
GP estimate
~0.65
Confirm
Patch 4
Observed
0.904
Disinfect
Patch 5
Observed
0.243
Clean
Patch 6
GP estimate
~0.30
Confirm
Patch 1
Observed
0.794
Disinfect
Patch 2
Observed
0.519
Monitor
Patch 3
GP estimate
~0.52
Confirm
3 patches → Disinfect 1 → Clean 1 → Monitor 4 → Confirm (human)
GP-estimated patches inherit elevated uncertainty and correctly trigger the human-confirmation rule (σᵢ > 0.3) rather than autonomous action.

## Slide 10
Human–Robot Collaboration Rules
Four threshold rules balance robot autonomy with human oversight
μᵢ > 0.7
Robot autonomously disinfects — no confirmation needed
σᵢ > 0.3
Robot pauses, flags patch, requests human inspection
Human detected nearby
UV source immediately paused for operator safety
μᵢ < 0.2 and σᵢ < 0.1
Patch certified clean, removed from priority queue

## Slide 11
Validation Plan
Current status: analytical validation. Next: simulation, then hardware.
Done
Closed-form Bayesian fusion derivation
RBF-kernel GP formulation
3×3 grid analytical case study
Sensitivity analysis (noise, length-scale, prior)
4 qualitative case studies + baseline comparison
Next
Python/MATLAB synthetic-field simulation
ROS 2 real-time map updates
Gazebo full-pipeline testing
Sparse GP for O(n³) scalability
Future
Real sensor noise calibration
Bayesian decision-theoretic HRC policy
3D surface extension
Hardware validation on mobile manipulator

## Slide 12
Literature gaps,
mapped to a rigorous method
Thank you — questions and discussion welcome.