## Slide 1
Session 1:RESEARCH PROPOSAL
Bayesian Sensor Fusion & Gaussian Process Mapping
for Human–Robot Collaborative Hygiene Monitoring and Surface Disinfection
Presented by : Group 1

## Slide 2
The Problem
Disinfection robots clean blindly — without knowing what's actually contaminated
No contamination sensing
Robots traverse a fixed path and irradiate or spray on schedule — without sensing whether contamination is actually present.
No verification
Systems confirm a UV lamp followed its planned path, not that pathogens were actually removed from the surface.
Operator carries the burden
With no probabilistic hygiene model, the human retains full cognitive responsibility for spotting contaminated areas.
Bottom line: contamination is spatially uneven, sensing is absent, and verification stops at geometry — not biology.

## Slide 3
The Research Gap
Five interrelated gaps in existing literature motivate this work
1
No automatic contamination estimation — systems detect surfaces, not contamination levels
2
Weak cleanliness verification — path execution confirmed, not biological cleanliness
3
Limited sensor fusion — visual, fluorescence, and dose data used in isolation
4
No continuous spatial hygiene map covering unobserved regions with calibrated uncertainty
5
HRC is perception-limited — humans retain full cognitive load for spotting contamination

## Slide 4
Proposed Solution
A unified Bayesian fusion + Gaussian Process hygiene mapping framework
Bayesian Sensor Fusion
Fuse Fluorescence and ATP sensor readings into a closed-form posterior, weighted by inverse variance. Fluorescence precision = 100, ATP precision = 50.
Gaussian Process Mapping
An RBF-kernel GP interpolates contamination across the full surface — observed and unobserved regions alike.
HRC Decision Policy
Uncertainty-aware priority scoring and threshold rules decide when the robot acts alone vs. defers to a human.
Result: a calibrated, full-coverage probabilistic hygiene map driving safe, explainable disinfection decisions.
Verifiable cleanliness
Quantified uncertainty

## Slide 5
System Architecture
Four sequential layers, from raw sensors to robot action
Sensing Layer
Fluorescence sensor (T1 Toilet, T2 Chair) and ATP sensor (T7 Door handle) — real measured RLU values from published research
Fusion Layer
Bayesian multi-sensor fusion → per-patch posterior mean & variance
Mapping Layer
GP regression with RBF kernel → full spatial hygiene map
Decision Layer
Priority scoring, UV dose, and HRC collaboration rules
Modular design: each layer can be updated or replaced independently without affecting the others.

## Slide 6
Validated Performance
Analytical results on a 3×3 surface-grid case study
87.3%
Uncertainty reduction — prior 0.09 to fused 0.011
2×
Fluorescence precision vs ATP — most accurate sensor
9 / 9
Full spatial coverage vs. 3/9 for Kalman filter
51.1%
Gaussian UV cleaning efficiency — T7 door handle 100% cleaned
Real sensor inputs: T1 Toilet = 0.75 (Fieldhouse 2025), T2 Patient chair = 0.13 (Fieldhouse 2025), T7 Door handle = 0.91 (Niephaus 2024). GP estimated 6 blocked tiles using RBF kernel. HRC decisions: T7 DISINFECT NOW, T1 CALL HUMAN, remainder MONITOR.
Important caveat: results are analytical/mathematical validation, not yet hardware-tested — simulation and physical deployment are the next steps.

## Slide 7
Why This Matters
Infection control
Moves disinfection robotics from blind path-following to evidence-based, verifiable cleaning.
Safer autonomy
Robots act independently only when confident, and defer to humans exactly where uncertainty is high.
Operational efficiency
Uncertainty-aware prioritization avoids wasting UV dwell time on already-clean regions.
Positioning
A mathematically rigorous foundation that is a natural, well-defined precursor to simulation (Python/ROS 2/Gazebo) and eventual hardware validation on a mobile manipulator platform.

## Slide 8
Roadmap
From mathematical model to hardware-validated system
1
NOW
Analytical Validation
Complete — closed-form math, 3×3 grid case study, sensitivity analysis.
2
NEXT
Simulation
MATLAB simulation complete — 11-step pipeline: Bayesian fusion, GP mapping (9/9 coverage), Kalman comparison, HRC decisions, Gaussian UV cleaning (51.1% efficiency).
3
THEN
Hardware Calibration
Real fluorescence/hyperspectral sensor calibration replacing assumed noise values.
4
FUTURE
Hardware Validation
Mobile manipulator deployment in a controlled hospital-room mock-up.

## Slide 9
A principled path toward
verifiable, autonomous hygiene monitoring
Thank you — questions and discussion welcome.