## Slide 1
Session 3:METHODOLOGY
Bayesian Sensor Fusion &
Gaussian Process Mapping
For Human–Robot Collaborative Hygiene Monitoring and Surface Disinfection
Case Study Assistive Robotics for Improvement Quality of Life
Presented by:
Alwa Jyoshna
Vallepu Vishnu
Kappala Mahesh

## Slide 2
SESSION OUTLINE
1
Research Problem Statement
2
Modelling Approach — Bayesian Sensor Fusion
3
Spatial Mapping — Gaussian Process Regression
4
Model Inputs, Assumptions & Data Sources
5
Decision Policy & HRC Rules
6
End-to-End Process Flowchart

## Slide 3
Existing Disinfection Robots:
Xenex Robot

## Slide 4
RESEARCH CONTEXT & PROBLEM STATEMENT
LIMITATIONS
No automatic contamination estimation
Shadowed areas may not receive UV light
Sensors used in isolation, not fused
No spatial hygiene map for unobserved areas
Full cognitive burden remains with operator
Proposed Framework Addresses:
Bayesian Fusion — Combines 4 sensor modalities optimally
GP Spatial Map — Covers observed + unobserved patches
Calibrated Uncertainty — Quantified confidence at every patch
HRC Decision Rules — Autonomy where safe, human input where uncertain
Cleanliness Verification — Probabilistic, not just path-level

## Slide 5
MAIN MODELLING APPROACH
LAYER 1
Sensing
Raw multi-modal data acquisition
Fluorescence (T1,T2) · ATP (T7)
LAYER 2
Bayesian Fusion
Precision-weighted posterior per patch
Closed-form Gaussian estimator
LAYER 3
GP Mapping
Spatial interpolation via RBF kernel
Full probabilistic hygiene map (9/9 coverage)
LAYER 4
Decision Policy
Priority score · UV exposure time
HRC collaboration rules
Each layer is independently modular and replaceable without affecting the others

## Slide 6
BAYESIAN MULTI-SENSOR FUSION — MODEL
Sensor Measurement Model
z_{m,i} = f_i + ε_m, ε_m ~ N(0, σ²_m)
Fluorescence
σ² = 0.01
T1 Toilet, T2 Chair — precision 100
ATP
σ² = 0.02
T7 Door handle — precision 50
Prior belief
σ² = 0.09
Neutral start (μ₀ = 0.5)
Fused variance
0.011
87.3% uncertainty reduction
Closed-Form Posterior
Posterior Precision:
σ⁻²_fused = σ⁻²₀ + Σ σ⁻²_m
Posterior Variance:
σ²_fused = 1 / (σ⁻²₀ + Σ σ⁻²_m)
Posterior Mean:
μ_fused = σ²_fused · (μ₀/σ²₀ + Σ z_m/σ²_m)
Key Property: σ²_fused < σ²_m for all m
→ Adding any sensor always reduces uncertainty

## Slide 7
GAUSSIAN PROCESS SPATIAL MAPPING
GP Prior
f(x) ~ GP( μ₀, k(x, x') )
RBF Kernel: k(xᵢ,xⱼ) = σ²_f · exp(−‖xᵢ−xⱼ‖²/2l²)
Length-scale l = 1.0, Signal variance σ²_f = 1.0
GP Posterior Equations
μ_* = K_*ᵀ (K + Σ_n)⁻¹ y
Σ_* = K_** − K_*ᵀ (K + Σ_n)⁻¹ K_*
Σ_n = diag(σ²_fused) from Bayesian fusion outputs
Hygiene Map — 3×3 Grid Example
T1
0.689
observed
T2
0.267
observed
T3
0.576
GP est.
T4
0.576
GP est.
T5
0.576
GP est.
T6
0.576
GP est.
T7
0.772
observed
T8
0.576
GP est.
T9
0.576
GP est.
Disinfect
Monitor
Clean
GP Only

## Slide 8
MODEL ASSUMPTIONS
A1
Gaussian Sensor Noise
Each sensor error ε_m ~ N(0, σ²_m). Enables closed-form Bayesian posterior. May not hold for fluorescence on complex surfaces — approximate Bayes (EP/VI) needed if violated.
A2
Spatial Smoothness (RBF Kernel)
Contamination is spatially correlated with smooth decay over distance. RBF chosen for mathematical tractability. Sudden discontinuities (e.g. sealed patches) require Matérn kernel.
A3
Contamination ∈ [0, 1]
Scalar bounded representation f_i ∈ [0,1]. Interpretable and compatible with both fusion and GP. Assumes all modalities can be normalised to this range prior to fusion.
A4
Independent Sensor Noise
Noise terms of different sensors are mutually independent. Simplifies the precision-sum formula. Cross-sensor correlations (e.g. both affected by lighting) would require a joint noise model.
A5
Stationary Contamination During Scan
Surface contamination does not change during a single robot traversal. Valid for single scans; requires recursive Bayesian / Kalman filter extension for continuous temporal monitoring.
A6
Known Sensor Noise Variances
σ²_m values are set from literature. In practice, these must be empirically calibrated from controlled experiments on known ground-truth surfaces before hardware deployment.

## Slide 9
REQUIRED INPUTS & DATA SOURCES
Input / Parameter
Type
Value / Source
Used In
Surface patch coordinates x_i
Model input
Integer grid {0,1,2}²
GP kernel
Prior mean μ₀
Model param.
0.5 (neutral belief)
Bayesian fusion
Prior variance σ²₀
Model param.
0.09 (literature)
Bayesian fusion
Fluorescence z_F (T1,T2)
Sensor data
900, 161 RLU (Fieldhouse 2025)
Fusion layer
ATP reading z_ATP (T7)
Sensor data
907 RLU (Niephaus 2024)
Fusion layer
Sensor noise variances σ²_m
Calibration
Literature / empirical
Fusion weights
GP length-scale l
Hyperparameter
1.0 (cross-validation)
RBF kernel
GP signal variance σ²_f
Hyperparameter
1.0 (normalised)
RBF kernel
Touch frequency T_i
Domain knowledge
Clinical / expert input
Priority score

## Slide 10
DECISION POLICY & HRC RULES
Priority Score
Pᵢ = w₁·μᵢ + w₂·σᵢ + w₃·Tᵢ
μᵢ = contamination estimate | σᵢ = uncertainty | Tᵢ = clinical importance
Adaptive UV Dose
D_req = D_base · (1 + λ·μᵢ + κ·σᵢ) → t_i = D_req / I_i
IF: μᵢ > 0.7
THEN: AUTONOMOUS DISINFECT
High-confidence contamination detected
IF: σᵢ > 0.3
THEN: REQUEST HUMAN INSPECT
Uncertainty too high for autonomous action
IF: Proximity detected
THEN: PAUSE UV → SAFETY
UV source halted until human clears area
IF: μᵢ < 0.2 & σᵢ < 0.1
THEN: CERTIFY CLEAN
Both contamination and uncertainty below threshold

## Slide 11
END-TO-END PROCESS FLOWCHART
1. Start: Robot Traversal Begins
2. Multi-Sensor Data Acquisition (RGB-D · Fluorescence · Hyperspectral · UV-dose)
3. Bayesian Fusion per Patch → (μ_fused, σ²_fused)
4. GP Regression over Surface → Full Hygiene Map H(xᵢ)
5. ◆ HRC Decision Rule Applied
DISINFECT
(μ > 0.7)
CONFIRM
(σ > 0.3)
PAUSE
(proximity)
CLEAN ✓
(μ<0.2)
6. Update Priority Queue & Map Log
7. All Patches Done? → End / Next Traversal

## Slide 12
KEY ANALYTICAL RESULTS
87.3%
Variance Reduction
vs Prior
2×
Fluorescence precision
vs ATP (100 vs 50)
9 / 9
Spatial Coverage
(vs 3/9 Kalman)
4
HRC Decision
Categories
Method Comparison
Method
MSE (Variance)
Coverage
Full Map
Prior only
0.09000
0/9
No
Fluorescence Only
0.01000
3/9
No
Kalman filter
0.00000
3/9
No
Bayesian Fusion
0.01145
3/9
No
Proposed (Bayes+GP)
0.00512*
9/9
Yes ✓
* At the 3 observed tiles. Kalman matches Bayesian fusion there but covers only 3/9; GP reaches all 9 tiles with bounded extra uncertainty.

## Slide 13
METHODOLOGY SUMMARY
Framework at a Glance
Sensing
2 sensors — Fluorescence (T1,T2) and ATP (T7), real RLU values
Fusion
Precision-weighted Bayesian posterior → 87.3% variance reduction
Mapping
RBF-kernel GP regression → 9/9 spatial coverage
Decision
Priority score + adaptive dose + 4 HRC collaboration rules
Analytical validation on 3×3 grid confirms mathematical feasibility — simulation & hardware validation as next steps